SimSys Corp.

WEEKLY REPORT (16.04.2007)

Due to technical problems encountered in the departmental servers, some of the tasks are delayed.

•	Compiler Module: ASM Lexer and Parser (Emre, Gulhan)

ASM grammar rules are defined using ANTLR. This includes ASM instructions, define statements, labels, include statements and constant declarations. Using lexer and parser generated by ANTLR, ASM file samples are compiled. Compiler successfully checked syntaxes and identified errors in case.

The lexer tokenizes the input and checks if the content of the file is consistent with ASM grammar. After all file is converted into a series of tokens, parser will evaluate semantics of the tokens. The user will be given meaningful error messages.

The AST generator is also implemented. All tokens are put into the tree data structure. The next step in the compiler module will be generating a symbol table and assembling the code by using a tree walker.

•	Editor and GUI Module (Ozgur)

The bugs discovered during usage of beta version are corrected. More features are added to the GUI package such as adding files into project, undo/redo operations, implementing functionality of toolbar buttons.

•	Project Module (Mahmut)

The projectManager module is implemented and integrated into program. With the feature added, new projects can be created and existing projects can be loaded. Also new files opened while a project is active are added into project's workspace. Different from the design, PIDE now has one active project at a time. Any action the user will perform will directly affect the active project (saving, opening a file). User will be able to switch active project to an existing project which will be listed in workspace panel as an inactive project. Bugs and inconsistencies will be eliminated during development and testing phases.