SimSys Corp.

WEEKLY REPORT (22.11.2006)

During last week, project members have conducted research on their assigned topics. Two meetings are held on Saturday and Tuesday. In these meetings, results derived from the research are discussed. Having a deeper understanding of internals of the modules of the system, the program features and use cases are revised.

Mahmut Aktaşoğlu:

Research on debuggers mainly consisted of searching an open-source debugger, analyzing it if it can be integrated into our system and understanding basics of common embedded systems debuggers. First of all, there are few debuggers designed for embedded systems. Those who does the job are using (or derived from) GNU’s open-source debugger GDB most of the time.

GDB seems to be a good candidate to integrate into PIDE for embedded debugging. However, there are seems to be some disadvantages for GDB. First of all, GDB is designed for higher level languages like C and C++. It can be used with assembly language too. But it is not designed to be a front panel for embedded systems. But with appropriate tuning, GDB is the first choice of many embedded systems IDEs. Second, the tuning may not be as easy as it is expected, though – considering the lack of our experience in integration and considerably huge source of GDB. GDB documentation is helpful in understanding GDB and altering the source code. Lastly, GDB supports much more functionality than we need. GDB is aimed to be support many configurations. So trying to integrate the whole system with many features that will not be used is cumbersome.

Emre Kültürsay:

The process of identification of the components to be simulated in the system is of primary importance. Every element of the PIC microcontroller should be discovered with all of their features. This would be the preliminary necessary step in achieving correct simulation.

The 16F877 PIC microcontroller is a very powerful device. It provides various subsystems for handling very different application domains. The interfaces of those systems are very simple, being controlled via a couple of bits in some special registers.

The major components to be simulated in the microcontroller are identified as follows:

CPU: 35 Instructions

Flash Program Memory: 8Kx14bit

RAM Data Memory: 368x8bit

EEPROM Data Memory: 256x8bit

Interrupts

Digital I/O

Timers

10-bit A/D converter

Analog Comparator

PWM

SSP-SPI-I2C-USART serial communication

PSP parallel communication

In Circuit Serial Programming

Watchdog Timer

Sleep Mode

Brown Out Reset

Indirect Addressing

Power up timer

Power on reset

Gülhan Serhat:

According to our work division, İ have concentrated on text editors used for programming languages. First, various text editors that are widely used in the world are analyzed such as vi, emacs, gedit, editor of visual studio, editor of MPLAB etc. This analysis helped to identify the necessary features expected from a text editor. These can be listed as syntax highlighting, auto complete functionality, coding tools, keyboard macros, etc. To investigate how these functionalities are achieved, an open source PIC IDE is searched and miSim, which is developed in Java, is downloaded. The java codes and the documentation of miSim help a lot to understand how to implement a text editor with required functionalities. Further analysis of these codes will be performed.

Özgür Çakmak:

This week I made research on the parser generator ANTLR.

•	I found Eclipse plug-in of ANTLR on the net and downloaded the trial version of it.

•	I started to read the ANTLR tutorial in order to understand the grammar of that parser generator.

•	I have joined the ANTLR interest mailing list.

Apart from these, I have attended the group meetings we held this week where we discussed the design report issues.