SimSys Corp.

WEEKLY REPORT (29.11.2006)

This week, the group members continued to work on the design of the project. The research work started previous week, which is about the main modules of the project, has been continued and meetings are performed on Thursday, Saturday and Tuesday. In these meetings, each group member explained the outcomes of the research to the other group members and the topics are elaborated. Moreover, the group worked on the design report. Use case diagrams are revised and finalized, first drafts of the class diagrams are prepared, and some brainstorm is performed about the sequence diagrams.

Below are some of the outcomes of the research performed by each group member.

Mahmut Aktaşoğlu:

The GDB debugger is the most commonly used open-source debugging tool for embedded systems. It is designed to be able to debug a system from a remote machine so it consists of two major subsystems: symbol-side which runs on the host machine and target-side which handles the target system. GDB also provides user an interface via command-line which may be considered another subsystem. The symbol side consists of object file readers, debugging info interpreters, symbol table management, source language expression parsing, type and value printing. The target side consists of execution control, stack frame analysis, and physical target manipulation. The user interface consists of several actual interfaces, plus supporting code. Key points that these subsytems deal with to debug a program are breakpoints, watchpoints, signal processing, single stepping, command interpreter, symbol handling and generating symbol tables.

One alternative to GDB embedded debugger is BedBug designed for Motorola microprocessors. It is more specific and less complicated compared to GDB but it seems to have only one release which is version 1.0. It may help to understand basic debugging functionality for an embedded sysyem. Another alternative is RedBoot debugger and bootstrap. It is designed to replace the existing debug/boot tools CygMon and GDB stubs. It provides a complete bootstrap environment, including network downloading and debugging. It may be worth the effort to examine deeply this debugger.

Emre Kültürsay:

The PIC microcontroller holds several features in it. The ports are multiplexed with a number of functions to house all those features with minimum number of pads. As the process of module identification has been started the previous week, further elaboration on other modules is performed.  On to the top of last week's work, explanations of the operation of some of the modules in the microcontroller are added.

To name a few, the memory of the device is divided into four banks. Those banks all contain some special function registers in the early addresses and general purpose registers in the later parts.

The input-output ports have many uses

. These ports not only are used for general digital I/O, but also for A/D converter inputs, Parallel Slave Port data and controls, Timer controls, serial communication interfaces, etc. Also, some pins are sources for interrupts. Modeling of the interrupt structure is in fact a complementary part of modeling the execution mechanism. The program counter, together with some special registers is pushed to stack on an interrupt and they should be popped to continue proper operation on return from interrupt handling function.

Gülhan Serhat:

Making a simple editor program is an easy task, however a source code editor should have many extra features to simplify the work of the user, and implementing these features is a complicated job. Some of these features are syntax highlighting, auto complete and providing ways to easily use the compiler, simulator and debugger if we think that it is a part of a complete IDE. If we think of the design of an editor, many java classes will be needed to achieve these tasks. Some work on the class diagram is performed to identify the attributes and methods. The finalized version will be available on the design report.

Furthermore, regarding the simulation of the CENG336 board, the peripheral components other than PIC to be simulated are identified. These are:

•		Power on LEDs

•		LEDs x 8

•		7 Segment Displays x 3

•		Keyboard

•		LCD

•		Reset button

•	  Parallel Port

•		Serial Port

•	  USART

•		Speaker

•		USB port

•	  Smart Card Reader

•		Jumpers (Oscillator, Programming)

Documentation on some of these components is present on the CENG336 course web page. Documentation about the others is requested from the course assistants. The design of these components will be worked out this week in group meetings.

Özgür Çakmak:

This week I made research on the parser generator ANTLR.

Our compiler will take an input source file, and output some executable. Let's divide it into tasks:

•	Lexical Analysis ( scanning )

•	Semantic Analysis ( parsing )

•	Tree Generation

•	Code Generation

•	Interpretation

The approach going to be taken is to generate a pseudo-machine code and to write a simple interpreter at the end.

Lexical Analysis : The compiler will read the input file and divide it into tokens.

Semantic Analysis: The compiler will evaluate the scanned tokens according to the grammar rules defined.

Tree Generation: An Abstract Syntax Tree(AST) will be stored using ANTLR's built-in

tree routines. This tree will behave like the communication device between the parser and the generator.

Code Generation: The code will be written by walking through the AST tree.

Interpretation: The interpreter will allow to test the compiled output without needing to learn specific machine code. ( This interpreter will be used during the development of our project. It will not be a permanent feature in our program ).

I'll be focusing on these basics in the forthcoming weeks.